## Slide 1: Number System and Computer Arithmetic

## Slide 2: Integer Representation
Integer
Signed
Unsigned
Sign and Magnitude
1’s Complement
2’s Complement

## Slide 3
Computers uses a fixed number of bits to represent an integer.
The commonly-used bit-lengths for integers are 8-bit, 16-bit, 32-bit or 64-bit.
Besides bit-lengths, there are two representation schemes for integers:
Unsigned Integers: can represent zero and positive integers.
Signed Integers: can represent zero, positive and negative integers.
Three representation schemes had been proposed for signed integers:
  Sign-Magnitude representation
  1's Complement representation
  2's Complement representation

## Slide 4: Unsigned Integers
Unsigned integers can represent zero and positive integers, but not negative integers. An n-bit unsigned integer can represent integers from 0 to (2^n)-1
n= number of bits | Minimum | Maximum
8 | 0 | (2^8)-1 (=255)
16 | 0 | (2^16)-1 (=65,535)
32 | 0 | (2^32)-1 (=4,294,967,295) (9+ digits)
64 | 0 | (2^64)-1 (=18,446,744,073,709,551,615) (19+ digits)

## Slide 5: Signed Integers Sign Magnitude Representation
The most-significant bit (msb) is the sign bit,
  0 representing positive integer
  1 representing negative integer.
The remaining n-1 bits represents the magnitude (absolute value) of the integer.

## Slide 6
This is not possible in number system.
so this is drawback of sign and magnitude representation method.
Therefore we use 2’s complement method to represent signed number
0 and -0 ?

## Slide 7: Signed Integers 1’s Complement Representation
Sign Bit | 1’s complement of actual binary

## Slide 8
1’s Complement Representation
Can represent numbers from -32,767 to 32,767.
    -215+1 .. 215-1
Arithmetic is easier than sign-magnitude.
But, still have two representations for zero:
    0 = 00000000 00000000
    -0 = 11111111 11111111

## Slide 9: Signed Integers 2’s Complement Representation
Sign Bit | 2’s complement of actual binary

## Slide 10: Signed Integers 2’s Complement Representation

## Slide 11: Binary Addition
Input Bits |  | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1+1+1=11
1+1+1+1=100

## Slide 12: Unsigned Binary Multiplication